Aremco Products, Inc.   				Information Phone: 845 268-0039

707-B Executive Blvd.        			Emergency Phone:   800-535-5053

Valley Cottage, NY    10989 							  845-268-0039

SECTION I - PRODUCT IDENTIFICATION

IDENTITY: Ceramabond 503                        10/10/01

SECTION II - IDENTITY INFORMATION/HAZARDOUS INGREDIENTS

Compound               CAS #       ACGIH TLV    OSHA PEL

Aluminum Oxide         1344-28-1   10 mg/m3       N/D

Mono Aluminum/         13530-50-2   2 mg/m3       N/D

Phosphate

Water                  N/A         N/A		  N/D

*NOTE:  The above listed compound is suspended in an inorganic binder

system, therefore no free dust exists.

HEALTH:  0	FLAMMABILITY:   0	REACTIVITY:   0

SECTION III - PHYSICAL DATA

Boiling Point: 			212 F

Specific Graviy: 		2.1

Vapor Density (AIR=1): 	No Data

Vapor Pressure (mm Hg.): 	No Data

Melting Point: 			No Data

Evaporation Rate: 		No Data (Butyl Acetate=1)

Solubility in Water: 		50%

V.O.C. content: 		0 gm/ltr

Appearance and Odor: 		Odorless, white viscous liquid.

SECTION IV - FIRE and EXPLOSION HAZARD DATA

Flash Point: 				N/A

Flammable Limits:			LEL: No Data  	UEL: No Data

Extinguishing Media: Not Flammable

Special Fire Fighting Procedures:

Use self contained air supplied breathing apparatus, and impervious protective

clothing.

Unusual Fire and Explosion Hazards:

Not considered a fire hazard and does not support combustion. When involved in a fire, does not contribute any unusual fire hazards.

SECTION V - REACTIVITY DATA

Stability:			(   ) Unstable     ( X ) Stable

Conditions to avoid:

Acidic in nature and reacts with bases, such as carbonates, oxides and hydroxides of alkali metals, to form insoluble hydrates of aluminum phosphate.

This material is corrosive to common metals such as mild steel, copper, brass, and bronze.

Hazardous Polymerization:   (   ) May Occur      ( X ) Will Not Occur

SECTION VI - HEALTH HAZARD DATA

Effects of Overexposure

Inhalation:

There are no known data available which address medical conditions that are generally recognized as being aggravated by exposure to this product.

Dermal Exposure:

Contact with skin may result in irritation or burns.

Eye Irritation:

Contact with eyes may result in irritation or burns.

Ingestion:

May cause stomach pains and nausea.

Emergency and First-Aid Procedures:

Eye:

Immediately flush with large quantities of water for at least 15 minutes.  Obtain medical attention as soon as possible.  Oils or ointments should not be used at this time.

Skin:

Flush affected areas with plenty of soap & water for several minutes.  Seek medical attention if skin irritation occurs.

Ingestion:

Give several glasses of water but do not induce vomiting.  if vomiting does occur, give fluids again.  Seek medical attention immediately.  Do not give anything by mouth to an unconscious or convulsing person.

Inhalation:

There are no known data available which addresses medical conditions that are

generally recognized as being aggrevated by exposure to this product.

SECTION VII - PRECAUTIONS FOR SAFE HANDLING AND USE

Steps to be taken in case material is released or spilled:

Neutralize the spill area with soda ash and then flush area with copious amounts of water.  Exercise caution during the neutralization as considerable heat may be generated.

Waste Disposal Method:

Dispose of in accordance with local, state, and federal regulations for corrosive materials. Precautions to be taken in handling and storing:  Containers should be stored in a cool, dry, well ventilated area away from flammable materials and sources of heat or flame.  Exercise due caution to prevent damage to or leakage from the container.

SECTION VIII SPECIAL PROTECTION INFORMATION

Use NIOSH approved mist respirator where spray occurs.  Use of impervious

rubber gloves and chemical goggles is recommended.

Good industrial hygiene practice requires that employee exposure be maintained below the recommended TLV.  This is preferably achieved through the provision of adequate ventilation where necessary.  Where  mist cannot be controlled in this way, personal respiratory protection should be employed.

CHEMICAL COMPONENTS OF THIS PRODUCT WHICH ARE PRESENT IN REPORTABLE AMOUNTS

AND ARE LISTED IN SECTION 313 OF THE EMERGENCY PLANNING AND COMMUNITY RIGHT  TO KNOW ACT OF 1986 (SARA TITLE III) ARE SHOWN BELOW WITH THEIR CAS REGISTRY NUMBERS AND MAXIMUM COMPOSITION BY WEIGHT.

LISTED CHEMICAL                 CAS NUMBER              MAX WT %

NONE

DISCLAIMER OF LIABILITY: THE INFORMATION CONTAINED HERE IN IS BASED ON DATA

TAKEN FROM SOURCES BELIEVED TO BE BOTH CURRENT AND RELIABLE AT THE TIME OF

PUBLICATION. AREMCO PRODUCTS, INC MAKES NO WARRANTIES EXPRESSED OR IMPLIED,

AS TO THE ACCURACY AND ASSUMES NO LIABILITY ARISING FROM ITS USE BY OTHERS.

COMPLIANCE WITH ALL APPLICABLE FEDERAL, STATE AND LOCAL LAWS AND REGULATIONS

REMAINS THE RESPONSIBILITY OF THE USERS.